## Slide 1: Convolution Reverb: Impulse responses of spaces
Katya Soltan and Anisha Nakagawa

## Slide 2: Dove in the AC Staircase
Impulse Response
of a staircase
Dove
Call
Dove in a staircase
*
=

## Slide 3: System Diagram
x(t)
y(t)
Finding the Impulse Response
Convolving with Sound
X(jw)
Y(jw)
H(jw) =
Y(jw)
X(jw)
h(t)
Input
Recording
Impulse Response
of the Space
-1
h(t) * s(t) = s’(t)
Impulse
Response
Original
Sound
Sound in the space

## Slide 4: Part 1: Find the Impulse Response

## Slide 5: Generating Impulse Responses: Instantaneous Sound
x(t)
y(t) = h(t)
h(t)
Input: Impulse
Impulse Response
of the Space
Output: Impulse Response
Ex. clap, gunshot
Downsides
You can’t make an ideal impulse
Susceptible to noise

## Slide 6: Generating Impulse Responses: White Noise
Cross-correlation of white noise to create an impulse
Cross-correlation
Measure of how similar two signals are based on displacement
Sliding dot product

## Slide 7: Generating Impulse Responses: White Noise
Cross-correlation of white noise to create an impulse
Cross-correlation of White Noise
White Noise: no similarity except for when signals are exactly lined up
White Noise
White Noise
Impulse
=
Time
Time
Time
Amplitude
Amplitude
Amplitude

## Slide 8: Generating Impulse Responses: White Noise
Cross-correlation of white noise to create an impulse
Cross-correlation of White Noise
White Noise: no similarity except for when signals are exactly lined up
Downsides
Very noisy results
h(t) = RYX / RXX
Output & Input
Input & Input
Impulse Response

## Slide 9: Generating Impulse Responses: Sine Sweep
“Chirp:” Sweep through all the frequencies
x(t)
y(t)
X(jw)
Y(jw)
H(jw) =
Y(jw)
X(jw)
h(t)
Chirp
20Hz - 20kHz
Recording
Impulse Response
of the Space
-1
Notes: Insert of chirp

## Slide 10
x(t) = Chirp
-1
y(t) = Recording
Y(jw) = F{recording}
X(jw) = F{chirp}
Time (s)
Amplitude
Time (s)
Amplitude
Frequency (Hz)
Amplitude
H(jw) = Y(jw)/X(jw)
Frequency (Hz)
Amplitude
Frequency (Hz)
Amplitude
h(t) = Impulse Response
Time (s)
Amplitude
Notes: Insert of chirp

## Slide 11: Understanding the Impulse Responses: Tubes
Sound must travel at least twice the length of the tube
Vibration Modes

## Slide 12: Length of a Cardboard Tube

## Slide 13: Length of a Cardboard Tube
2 * L = T * 343 m/s
L = 1.4 m

## Slide 14: Length of a Cardboard Tube
2 * L = T * 343 m/s
L = 1.4 m
Actual Length:
1.39 m

## Slide 15: Length of a Short PVC Pipe
2 * L = T * 343 m/s
L = 0.89 m

## Slide 16: Length of a Short PVC Pipe
2 * L = T * 343 m/s
L = 0.89 m
Actual Length:
0.865 m

## Slide 17: Length of a Long PVC Pipe
2 * L = T * 343 m/s
L = 1.54 m

## Slide 18: Length of a Long PVC Pipe
2 * L = T * 343 m/s
L = 1.54 m
Actual Length:
1.52 m

## Slide 19: Impulse Responses of Spaces: AC Staircase
H(jw)
h(t)

## Slide 20: Impulse Responses of Spaces: The Oval
H(jw)
h(t)

## Slide 21: Part 2: Convolve the Impulse Response with Sounds
h(t) * s(t) = s’(t)
Impulse
Response
Original
Sound
Sound in the space

## Slide 22: Effect of Impulse Responses on a Sound: Cosine
Create an impulse response from a cosine
(Frequency of 300 Hz)
Frequency (Hz)
Amplitude
Original Dove
Time (s)
Amplitude
H(jw)
Notes: Include sounds

## Slide 23: Effect of Impulse Responses on a Sound: Cosine
Create an impulse response from a cosine
(Frequency of 300 Hz)
Time (s)
Amplitude
Original Dove
New Sound
Time (s)
Amplitude
Time (s)
Amplitude
300Hz
30Hz
3kHz
y(t) zoomed in
Notes: Include sounds

## Slide 24: Effect of Impulse Responses on a Sound: Box
Create an impulse response from a box
(Frequency of 5kHz - 10kHz)
Frequency (Hz)
Amplitude
Original Dove
New Sound
Time (s)
Amplitude
Time (s)
Amplitude

## Slide 25: Convolving Doves with a Skyline
Boston
Paris
Frequency (Hz)
Amplitude
Frequency (Hz)
Amplitude
Notes: Include sound

## Slide 26: Convolving Delitos with a Skyline
Boston
Barcelona
Frequency (Hz)
Amplitude
Frequency (Hz)
Amplitude
Notes: Include sound

## Slide 27: Convolving Sound with a Space
Tube Pumpkin
Sphere AC Stairs
Middle of the O
AC Stairs
DOVE
DELITOS